## Slide 1
Mapping TRANSEC onto the Wireless Spectrum
A physical-layer taxonomy of transmission-security objectives across bands
LPD
Low Probability of Detection
LPI
Low Probability of Intercept
LPE
Low Probability of Exploitation
AJ
Anti-Jam
TFS
Traffic Flow Security
Companion to “Wireless Communication Bands” · restricted to the physical layer · COMSEC out of scope
Nicholas D. Redmond · University of Memphis · July 2026
Notes: This is the taxonomy proper. Two axes: transmission-security objectives (columns) and bands (rows). The claimed contribution is the unification, not any single cell.

## Slide 2
Five TRANSEC objectives
Transmission security protects the transmission itself — not the message content (that is COMSEC)
LPD
Low Probability of Detection
Adversary cannot tell a transmission is happening at all.
Defeats: energy detection, spectrum surveillance.
Grounded in the covert-communications square-root law (Bash et al., 2013).
LPI
Low Probability of Intercept
Even if detected, adversary cannot determine it is a signal of interest or recover its parameters.
Defeats: parameter analysis, signal sorting.
CNSSI 4009 frames LPI as resisting analysis of transmission parameters.
LPE
Low Probability of Exploitation
Even if intercepted and characterized, adversary cannot derive intelligence from it.
Defeats: content and externals recovery at the PHY layer.
Wiretap-channel secrecy (Wyner, 1975); artificial noise (Goel & Negi, 2008).
AJ
Anti-Jam
Communication survives deliberate interference.
Defeats: barrage, partial-band, and follower jamming.
Spread spectrum and spatial nulling (Pirayesh & Zeng, 2022).
TFS
Traffic Flow Security
Traffic externals — presence, volume, timing, endpoints — are concealed from analysis.
Defeats: traffic analysis, pattern-of-life inference.
Emission control, cover traffic. Thinly studied at the PHY layer.
Refs: CNSSI No. 4009 (2022) · Bash, Goeckel & Towsley, IEEE JSAC 31(9) (2013) · Wyner, BSTJ 54 (1975) · Goel & Negi, IEEE TWC 7(6) (2008) · Pirayesh & Zeng, IEEE COMST 24(2) (2022).
Notes: Keep the COMSEC/TRANSEC boundary explicit up front — the most common reviewer objection is 'isn't this just a PLS survey.' LPE is the pillar closest to PLS; note it is exploitation resistance at PHY, distinct from encryption.

## Slide 3
Taxonomy structure
Each cell asks: for this band, how is this objective achieved — and how mature is it?
OBJECTIVE (what security goal)
LPD · LPI · LPE · AJ · TFS
MECHANISM (how it is achieved at PHY)
spreading · hopping · power control · beam confinement · spatial nulling · wiretap coding · artificial noise · absorption · emission control
BAND (where it lives)
NFC · Bluetooth · Wi-Fi · cellular 3G–6G · SATCOM (LEO/MEO/GEO, civil + military)
MATURITY RATING (cell fill)
N
Native — propagation or design gives it
E
Engineered — deployed, known mechanism
R
Research — emerging or proposed
W
Weak / absent
Notes: The mechanism layer is what makes this a taxonomy and not a scorecard: the same objective is reached by different mechanisms in different bands, and some mechanisms only exist at certain bands.

## Slide 4
The mapping
Physical-layer TRANSEC maturity by band and objective
N
E
R
W
LPD
LPI
LPE
AJ
TFS
NFC
near-field decay
proximity only
—
close-range only
—
Bluetooth / BLE
low power
public hop seq
—
AFH = coexist
RPA (link only)
Wi-Fi
beacons broadcast
standardized
PHY key gen
DFS ≠ AJ
open
Cellular 3G / 4G
3G gain modest
sync broadcast
—
3G DSSS partial
—
Cellular 5G NR
beam confinement
beam incidental
MIMO null + AN
spatial nulling
—
6G / sub-THz
absorption+pencil
narrow beam
UM-MIMO / RIS
pencil off-axis
proposed
SATCOM — civil
wide footprint
DVB-S2X open
—
limited
—
SATCOM — military
spread spectrum
EHF secret hop
noise-like signal
null + FHSS
continuous carrier
LPE = physical-layer exploitation resistance (wiretap coding, artificial noise, PHY key generation). Upper-layer cryptography (COMSEC) is out of scope, so civil systems that rely on it read as weak here.
Notes: Read the structure, not the individual cells: the military-SATCOM row is the only full row of Engineered; the 5G/6G block is the Research cluster; the TFS column is nearly empty; civil terrestrial bands are weak at PHY because their security lives in COMSEC, which is out of scope.

## Slide 5
Low Probability of Detection
Hiding that a transmission exists at all
LPD
How it is achieved, low band → high band
NFC: near-field magnetic decay (~1/r³) makes emission undetectable past ~1 m — physics supplies LPD for free.
3G DSSS: processing gain spreads energy toward the noise floor — a modest, code-public form of hiding.
5G mmWave: beamforming confines energy to a narrow cone — a warden off-axis observes nothing (spatial LPD).
6G sub-THz: molecular absorption plus pencil beams limit detection in both angle and range (propagation LPD).
Military SATCOM: engineered spread-spectrum downlinks push emissions below detectability for off-target receivers.
Where it is strong
Near-field (NFC) and the mmWave/THz frontier, where geometry and absorption do the work.
Protected military SATCOM, by deliberate spread-spectrum design.
Where it fails or is missing
All civil terrestrial radio designed to be found: Wi-Fi beacons, cellular sync signals, BLE advertising.
Deployment lags theory: the square-root law is well developed, fielded civil LPD is not.
THz LPD is not automatic — a scatterer in the beam re-enables eavesdropping (Ma et al., 2018).
Taxonomic reading: LPD moves from a signal-domain mechanism (spreading) at low bands to a propagation/spatial mechanism (beams, absorption) at high bands — the band axis changes which mechanism is even available.
Refs: Bash, Goeckel & Towsley, IEEE JSAC 31(9) (2013) · Chen et al., IEEE COMST 25(2) (2023) · Ma et al., Nature 563 (2018).
Notes: LPD is the theory-rich, deployment-poor column. The interesting taxonomic content is the low-to-high mechanism shift.

## Slide 6
Low Probability of Intercept
Detected, but not identifiable as a signal of interest
LPI
How it is achieved, low band → high band
Frequency hopping with a secret sequence: the observer sees energy but cannot predict where it goes next.
Direct-sequence spreading with a secret code: the waveform looks noise-like without the code.
Waveform / parameter randomization: deny the constant features a sorter keys on.
Beam directionality (5G/6G) adds incidental LPI — only a receiver in the beam can even attempt analysis.
Military EHF SATCOM: secret hop patterns are the reference implementation of fielded LPI.
Where it is strong
Military systems using secret spreading / hopping — the intended home of LPI.
Where it fails or is missing
Every civil standard: hop sequences and spreading codes are published for interoperability, so parameters are recoverable by design.
Bluetooth AFH and cellular hopping exist for coexistence, not concealment — they do not deny parameter analysis.
Taxonomic reading: LPI is almost entirely a military column. Civil interoperability requires published parameters, which is the opposite of LPI — the one objective where the commercial/defense split is sharpest.
Refs: CNSSI No. 4009 (2022) · Pirayesh & Zeng, IEEE COMST 24(2) (2022).
Notes: Draw the interoperability-vs-secrecy tension explicitly: it is why LPI does not migrate into civil bands even as hardware improves.

## Slide 7
Low Probability of Exploitation
Intercepted and characterized, but still yields no intelligence
LPE
How it is achieved, low band → high band
Wiretap-channel coding: exploit a channel advantage so the eavesdropper's equivocation stays high (Wyner, 1975).
Artificial noise: spend power to degrade only the eavesdropper's channel, not the intended one (Goel & Negi, 2008).
MIMO / massive-MIMO beamforming: steer a spatial null toward the eavesdropper (5G, and 6G ultra-massive arrays).
Channel-based key generation: derive shared keys from reciprocal channel randomness at the PHY layer.
RIS-aided nulling (6G): reshape the environment to suppress the eavesdropper's received signal.
Where it is strong
Multi-antenna bands (5G/6G): spatial degrees of freedom make secrecy and artificial noise practical.
Military SATCOM: noise-like spread signals leak little from their externals.
Where it fails or is missing
Single-antenna, low-band systems (NFC, BLE, legacy cellular) have few PHY degrees of freedom to exploit.
Most academic PLS work stops at simulation; reciprocity and CSI assumptions rarely survive deployment.
Taxonomic reading: LPE is where the academic PLS literature concentrates, and it scales with spatial degrees of freedom — which is exactly why it strengthens as bands rise and arrays grow.
Refs: Wyner, BSTJ 54 (1975) · Goel & Negi, IEEE TWC 7(6) (2008).
Notes: This is the pillar closest to mainstream PLS. Keep it framed as transmission-security exploitation resistance, and note the simulation-to-deployment gap so peers see the honesty.

## Slide 8
Anti-Jam
Communication that survives deliberate interference
AJ
How it is achieved, low band → high band
Spread-spectrum processing gain: DSSS/FHSS raise the jammer's required power by the spreading factor.
Frequency hopping: move faster than a follower jammer can track.
Spatial nulling: adaptive antennas and massive MIMO place pattern nulls on the jammer (5G/6G).
Pencil beams (6G/THz): an off-axis jammer contributes almost no power into the beam.
Military SATCOM: nulling antennas plus EHF hopping are the fielded gold standard.
Where it is strong
Military SATCOM and tactical radios — the best-developed TRANSEC column overall.
Multi-antenna 5G/6G, where spatial nulling adds a new anti-jam axis.
Where it fails or is missing
GNSS: low received power makes it notoriously jammable; CRPA antennas only partly help.
Civil Wi-Fi and cellular have little intrinsic AJ — DFS and power control are not jam resistance.
Pencil-beam AJ trades one weakness for another: robust off-axis, but fragile to blockage.
Taxonomic reading: AJ is the most mature objective across the whole matrix, and the only one with both a deep signal-domain toolkit and a growing spatial one — the two regimes reinforce rather than replace each other here.
Refs: Pirayesh & Zeng, IEEE COMST 24(2) (2022) · Tedeschi, Sciancalepore & Di Pietro, Computer Networks 216 (2022).
Notes: Use GNSS as the cautionary counterexample: a globally deployed system with a first-order AJ weakness, showing that maturity of the field does not mean every system is protected.

## Slide 9
Traffic Flow Security
Concealing traffic externals — the sparse column
TFS
How it is achieved, low band → high band
Emission control (EMCON): transmit only when necessary to deny a pattern of life.
Cover / dummy traffic: keep emission constant so real activity is not distinguishable from idle.
Constant-envelope continuous carriers: hide volume and timing behind a steady signal.
Decoy-channel and dual-messaging schemes: emit structured traffic that masks the real channel (an active research direction).
Address / identifier randomization (e.g. BLE RPA) partly hides endpoints — but at the link layer, not the PHY.
Where it is strong
Military SATCOM and naval EMCON doctrine, where continuous-carrier and radio-silence practices are established.
Where it fails or is missing
Nearly every civil band: traffic timing and volume are exposed by design.
PHY-layer TFS is thinly studied — most traffic-analysis defense lives at the network / anonymity layer, not the waveform.
Taxonomic reading: TFS is the empty column of the taxonomy at the physical layer — the clearest gap, and the strongest place for a new contribution (including PHY-layer dual-messaging / decoy-channel work).
Refs: CNSSI No. 4009 (2022) · Chen et al., IEEE COMST 25(2) (2023, network-layer covert channels).
Notes: Be candid that this column is where the literature is weakest at PHY. This is the opening for the FHODM dual-messaging line of work to sit inside the taxonomy as a genuine contribution rather than a repackaging.

## Slide 10
Two mechanism regimes
The band axis does not just add bandwidth — it changes which TRANSEC mechanisms physically exist
SIGNAL-DOMAIN REGIME
Low bands — NFC through sub-6 cellular
Security is built in the waveform: spreading, hopping, coding, power control.
Objectives served: AJ and LPI (with secret parameters), some LPD via processing gain.
Ceiling: narrow bandwidth caps spreading gain; a single antenna offers no spatial handle.
PROPAGATION / SPATIAL REGIME
High bands — mmWave and sub-THz
Security comes from geometry and physics: pencil beams, spatial nulls, molecular absorption.
Objectives served: LPD and LPE by confinement, AJ by off-axis rejection.
Ceiling: blockage and range fragility; a scatterer can undo the confinement (Ma et al., 2018).
The transition band matters most. 5G FR1→FR2 and the 7–24 GHz upper mid-band are where a system can draw on both regimes at once — the richest, least-mapped region of the taxonomy.
Notes: This is the single strongest taxonomic claim in the deck: the two regimes are not a spectrum of degree but two different physical toolboxes, and the mid-band overlap is where both are available.

## Slide 11
Gaps and contribution
What the matrix shows is missing — and what unifying it adds
Empty and thin cells
TFS at the PHY layer is nearly empty across every band — the clearest single gap.
LPD deployment trails LPD theory badly outside military systems.
LPI does not exist in civil bands and structurally cannot, given interoperability.
What the unified view adds
Imports the CNSSI TRANSEC frame to organize a literature currently split across covert-comms, PLS, and anti-jam surveys.
Makes band a first-class axis, exposing the two-regime structure and the mid-band overlap.
Names military SATCOM as the only full-stack exemplar to measure civil systems against.
Positioning vs. existing surveys
Covert-comms surveys cover one column (LPD); anti-jam surveys cover another (AJ).
SATCOM and THz security surveys cover one band region each.
None spans all five objectives across all bands at the PHY layer — the contribution is the unification.
Claim: not a new mechanism, but the first physical-layer TRANSEC taxonomy that maps all five objectives across the full band range — with TFS-at-PHY as the open frontier.
Notes: Anticipate the 'isn't this a PLS survey' objection here again, and answer with the column/band coverage argument the survey stream cannot match.

## Slide 12
References
FOUNDATIONS & DEFINITIONS
C. E. Shannon — “Communication Theory of Secrecy Systems,” Bell System Technical Journal, vol. 28, 1949.
A. D. Wyner — “The Wire-Tap Channel,” Bell System Technical Journal, vol. 54, no. 8, pp. 1355–1387, 1975.
CNSS — CNSSI No. 4009, Committee on National Security Systems Glossary (TRANSEC, LPI, AJ definitions), 2022.
OBJECTIVE-SPECIFIC MECHANISMS
B. A. Bash, D. Goeckel, D. Towsley — “Limits of Reliable Communication with Low Probability of Detection on AWGN Channels,” IEEE JSAC, vol. 31, no. 9, 2013. [LPD]
S. Goel, R. Negi — “Guaranteeing Secrecy using Artificial Noise,” IEEE Trans. Wireless Communications, vol. 7, no. 6, pp. 2180–2189, 2008. [LPE]
H. Pirayesh, H. Zeng — “Jamming Attacks and Anti-Jamming Strategies in Wireless Networks: A Comprehensive Survey,” IEEE Communications Surveys & Tutorials, vol. 24, no. 2, 2022. [AJ]
X. Chen et al. — “Covert Communications: A Comprehensive Survey,” IEEE Communications Surveys & Tutorials, vol. 25, no. 2, 2023. [LPD / TFS-adjacent]
BAND CONTEXT
P. Tedeschi, S. Sciancalepore, R. Di Pietro — “Satellite-based communications security: A survey of threats, solutions, and research challenges,” Computer Networks, vol. 216, 2022.
J. Ma et al. — “Security and eavesdropping in terahertz wireless links,” Nature, vol. 563, pp. 89–93, 2018.
T. S. Rappaport et al. — “Wireless Communications and Applications Above 100 GHz,” IEEE Access, vol. 7, 2019.
Notes: Band-technology standards (ISO/IEC 18092, IEEE 802.11be, 3GPP TS 38.211, ETSI EN 302 307-2, ITU-R M.2160) are carried in the companion survey deck and are not repeated here.