## Slide 1
Wireless Communication Bands
A physical-layer survey: NFC to terahertz, ground to orbit
Foundation for a physical-layer TRANSEC taxonomy across all wireless bands
10 MHz
100 MHz
1 GHz
10 GHz
100 GHz
1 THz
NFC
BT / Wi-Fi
Cellular sub-6
SATCOM Ku/Ka
5G mmWave
6G sub-THz
Nicholas D. Redmond · University of Memphis · July 2026
Notes: Scope framing: every band slide follows the same physical-layer attribute set so bands can be compared column-for-column later in the taxonomy.

## Slide 2
NFC — Near-Field Communication
Coupling, not radiating: communication via a shared magnetic field
13.56 MHz · λ ≈ 22 m · range < 10 cm
10M
100M
1G
10G
100G
1T
Hz
FREQUENCY & RANGE
13.56 MHz (HF ISM band)
λ ≈ 22 m, but operating range < 10 cm
Device sits deep inside the near field (r ≪ λ/2π)
WAVE CHARACTERISTICS
Inductive magnetic coupling — no propagating far-field link
Field strength decays ~1/r³ → range is physics-limited
Reader and tag behave as a loosely coupled transformer
MODULATION & ACCESS
ASK (10% / 100%) with Miller or Manchester coding
Passive tag replies by load modulation of the reader field
106 / 212 / 424 kbps; simple reader-talks-first access
POWER
Passive tags harvest all power from the reader field
Reader field power ~100–500 mW
Zero-battery operation on the tag side
NOISE & INTERFERENCE
Near-field link → largely immune to far-field RF interference
Detuned by nearby metal; orientation-sensitive
Eavesdropping demonstrated at meters despite cm-range design
ANTENNA PROPERTIES
Loop coil (magnetic antenna) — not a resonant λ-scaled radiator
Flat printed spirals in cards and phone housings
Coil geometry sets coupling, not gain
APPLICATIONS
Contactless payment (EMV), transit, access control
Passive tags and smart posters
Pairing bootstrap for Bluetooth / Wi-Fi
BENEFITS & LIMITATIONS
+ Proximity acts as built-in access control; passive, cheap
− Centimeter range, kbps rates
→ Anything beyond touch-range or low-rate needs a radiating band
Refs: ISO/IEC 18092:2013 / ECMA-340, NFC Interface and Protocol (NFCIP-1).
Notes: Key teaching point: NFC is the one 'band' here that is not a radio link in the far-field sense. Good anchor for why wavelength vs. range matters.

## Slide 3
Bluetooth / BLE
Low-power personal-area links in the crowded 2.4 GHz ISM band
2.400–2.4835 GHz · λ ≈ 12.5 cm · 1–100 m
10M
100M
1G
10G
100G
1T
Hz
FREQUENCY & RANGE
2.400–2.4835 GHz (global unlicensed ISM)
Classic: 79 × 1 MHz channels; BLE: 40 × 2 MHz
Range 1–100 m depending on power class
WAVE CHARACTERISTICS
UHF far-field; moderate wall penetration
Rich indoor multipath; narrowband channels fade flat
Body shadowing matters at wearable power levels
MODULATION & ACCESS
GFSK (BLE / BR); π/4-DQPSK and 8DPSK for EDR (≤3 Mbps)
FHSS at 1600 hops/s (Classic); adaptive hopping in BLE
TDD master–slave scheduling — an early consumer TRANSEC relative
POWER
Class 1: 100 mW · Class 2: 2.5 mW · Class 3: 1 mW
BLE duty-cycled to ~µW–mW average
Years on a coin cell is the defining design target
NOISE & INTERFERENCE
Shares 2.4 GHz with Wi-Fi, Zigbee, microwave ovens
Adaptive frequency hopping blacklists occupied channels
Interference-limited, not noise-limited, in practice
ANTENNA PROPERTIES
Chip, PIFA, or meander antennas — λ small enough to embed
Near-omnidirectional, ~0 dBi
No aperture to spare → link budget leans on receiver sensitivity
APPLICATIONS
Audio, HID peripherals, wearables
BLE beacons, sensors, mesh lighting
Automotive keys, medical devices
BENEFITS & LIMITATIONS
+ Ultra-low power, negligible cost, ubiquitous
− ≤3 Mbps, short range, ISM congestion
→ Throughput and coverage needs push to Wi-Fi / cellular
Refs: Bluetooth SIG, Bluetooth Core Specification v6.1, May 2025.
Notes: FHSS in Bluetooth was interference-avoidance rather than security, but it is the same mechanism family as military TRANSEC hopping — worth one sentence when presenting.

## Slide 4
Wi-Fi (802.11)
High-throughput local access across three unlicensed bands
2.4 / 5 / 6 GHz (+60 GHz) · channels 20→320 MHz
10M
100M
1G
10G
100G
1T
Hz
FREQUENCY & RANGE
2.4 GHz, 5 GHz, 6 GHz (Wi-Fi 6E/7); 60 GHz in 802.11ad/ay
Channel widths 20 → 320 MHz (Wi-Fi 7)
~50–100 m indoors; 2.4 GHz reaches farthest
WAVE CHARACTERISTICS
Indoor multipath-rich, frequency-selective channels
OFDM subcarriers turn one hard channel into many easy ones
5/6 GHz penetrate walls worse than 2.4 — range/rate trade
MODULATION & ACCESS
OFDM / OFDMA; up to 4096-QAM in Wi-Fi 7
MU-MIMO spatial multiplexing
CSMA/CA listen-before-talk — polite, but contention-bound
POWER
~100 mW–1 W EIRP under regulatory caps
APs mains-powered; clients battery-constrained
Target-wake-time (Wi-Fi 6) trims client energy
NOISE & INTERFERENCE
Unlicensed → co-channel contention is the real limit
DFS radar-avoidance constraints at 5 GHz
Dense deployments become interference-limited
ANTENNA PROPERTIES
2×2 up to 8×8 MIMO; omni dipoles in APs
Implicit beamforming from channel sounding
Spatial streams, not aperture, drive capacity
APPLICATIONS
LAN access everywhere; cellular offload
Mesh backhaul, fixed wireless in unlicensed bands
60 GHz: AR/VR links, wireless docking
BENEFITS & LIMITATIONS
+ Multi-Gbps at consumer cost, universal adoption
− No guaranteed QoS; contention collapses under load; limited range
→ Wide-area coverage and mobility are cellular's job
Refs: IEEE Std 802.11be-2024, Enhancements for Extremely High Throughput (Wi-Fi 7), published Jul. 2025.
Notes: Bridge slide: Wi-Fi 7's 320 MHz channels preview the theme of the whole deck — capacity comes from bandwidth, and bandwidth lives up-spectrum.

## Slide 5
Cellular I: 3G → 4G
From spread-spectrum sharing to orthogonal subcarriers
600 MHz – 3.5 GHz licensed spectrum
10M
100M
1G
10G
100G
1T
Hz
3G — UMTS / WCDMA (≈2001)
Bands: 850–2100 MHz; 5 MHz carriers
Access: DSSS CDMA at 3.84 Mcps — all users share the band, separated by code
Modulation: QPSK → 16-QAM (HSPA); 0.4–42 Mbps (HSPA+)
PHY machinery: RAKE receivers combine multipath; soft handover; fast power control fights the near–far problem
Power: UE up to 24 dBm, tightly controlled — every user is everyone else's interference
Antenna: sector antennas at cell sites; single antenna in handsets
4G — LTE / LTE-A (≈2010)
Bands: 600 MHz–3.5 GHz; 1.4–20 MHz carriers + aggregation to 100 MHz
Access: OFDMA downlink; SC-FDMA uplink (lower PAPR spares the handset PA)
Modulation: up to 256-QAM; 2×2–4×4 MIMO; 100 Mbps–1 Gbps class
PHY machinery: cyclic prefix + per-subcarrier equalization replace RAKE; all-IP flat network
Power: UE 23 dBm; eNB tens of watts per sector
Antenna: cross-polarized sector arrays; MIMO becomes the capacity engine
WHY 3G → 4G
CDMA capacity is intra-cell-interference-limited: every added user raises the noise floor for all others, and wider bandwidth makes RAKE multipath combining harder. OFDMA sidesteps both — orthogonal subcarriers eliminate in-cell interference and make equalization trivial, so bandwidth and MIMO order can scale. Applications made the jump non-optional: smartphone video needed tens of Mbps, not hundreds of kbps.
Refs: 3GPP TS 25.211, UTRA (FDD): Physical channels and mapping · 3GPP TS 36.211, E-UTRA: Physical channels and modulation.
Notes: The 3G-to-4G transition is the cleanest example in the deck of an access-scheme change driven by a capacity ceiling rather than by new spectrum.

## Slide 6
Cellular II: 5G NR
One air interface stretched from 600 MHz to mmWave
FR1: 0.41–7.125 GHz · FR2: 24–71 GHz
10M
100M
1G
10G
100G
1T
Hz
FREQUENCY & RANGE
FR1 (sub-6/7): coverage + capacity workhorse
FR2 (mmWave, λ ≈ 4–12 mm): 400 MHz channels
FR2 cells: ~100–500 m outdoor, LOS-favored
WAVE CHARACTERISTICS
FR2 is quasi-optical: hands, bodies, foliage block it
O₂ absorption near 60 GHz; rain fade grows with f
Diffraction stops helping → blockage becomes the channel model
MODULATION & ACCESS
CP-OFDM, flexible numerology (15–120 kHz subcarriers)
Up to 256-QAM; scalable slots for URLLC (~1 ms)
Beam management is part of the access procedure itself
POWER
UE 23–26 dBm; gNB arrays concentrate watts into beams
Beamforming gain claws back mmWave path loss
Energy per bit improves even as absolute power rises
NOISE & INTERFERENCE
Wide channels → thermal-noise-limited (kTB grows with B)
Phase noise becomes a real impairment at FR2
Dense reuse managed by beams, not just cell planning
ANTENNA PROPERTIES
Massive MIMO (e.g., 64T64R) standard at mid-band
λ ≈ 1 cm → phased arrays fit inside a phone edge
Aperture scaling is the whole reason mmWave works at all
APPLICATIONS
eMBB, fixed wireless access, private industrial 5G
URLLC: automation, vehicular
mMTC: massive sensor populations
BENEFITS & LIMITATIONS
+ Multi-Gbps, low latency, network slicing
− FR2 coverage is tiny and fragile → densification cost
→ Mid-band carries most real traffic; mmWave stays a hotspot tool
Refs: 3GPP TS 38.211, NR: Physical channels and modulation · ITU-R Rec. P.676-12, Attenuation by atmospheric gases (2019).
Notes: Honest framing for an academic audience: FR2 deployment underperformed the 2019-era hype; the mid-band + massive MIMO combination is what actually delivered. That lesson previews the 6G/THz slide.

## Slide 7
Cellular III: 6G and the sub-THz frontier
Research territory: enormous bandwidth, unforgiving physics
7–24 GHz mid-band + 100–300 GHz research
10M
100M
1G
10G
100G
1T
Hz
FREQUENCY & RANGE
Upper mid-band 7–24 GHz: likely first 6G spectrum
Sub-THz 100–300 GHz (λ ≈ 1–3 mm): target 100 Gbps–1 Tbps
Sub-THz range: meters to a few hundred meters
WAVE CHARACTERISTICS
Molecular (H₂O) absorption lines carve usable spectral windows
Quasi-optical; scattering off surface roughness matters
Absorption limits eavesdropping distance — a TRANSEC upside
MODULATION & ACCESS
Candidates: OFDM variants, single-carrier + equalization, OTFS
ISAC: one waveform for sensing and communication
Nothing standardized — waveform choice is an open problem
POWER
PA efficiency collapses toward sub-THz (semiconductor limits)
Energy-per-bit, not peak rate, is the binding constraint
Photonic and hybrid front-ends under active research
NOISE & INTERFERENCE
Hardware impairments + phase noise rival thermal noise
Molecular absorption re-emission adds a noise floor
Interference scarce — beams are pencils, cells are bubbles
ANTENNA PROPERTIES
Ultra-massive arrays: 100s–1000s of elements in cm²
Pencil beams; near-field effects enter the link budget
RIS proposed to route around blockage
APPLICATIONS
Wireless backhaul / fronthaul at fiber-class rates
Short-range Tbps links, kiosk / chip-to-chip
Joint sensing + comms (ISAC)
BENEFITS & LIMITATIONS
+ Contiguous GHz-scale bandwidth exists nowhere else
− Range, blockage, PA efficiency, immature hardware
→ Likely niche links + densification, not blanket coverage
Refs: ITU-R Rec. M.2160-0 (11/2023) · Rep. ITU-R M.2541 (2024) · Rappaport et al., IEEE Access 7 (2019) · Ma et al., Nature 563 (2018).
Notes: Flag as research-stage throughout — 6G spectrum is not finalized (WRC-27 agenda). The absorption-aided covertness point connects directly to the THz column of the TRANSEC taxonomy.

## Slide 8
Satellite Communications I: Orbits
Altitude sets everything: delay, Doppler, coverage, constellation size
160 km → 35,786 km
LEO
160–2,000 km (Starlink ≈ 550 km)
Round-trip latency ~20–40 ms — terrestrial-class
Satellite moves ~7.6 km/s → large, fast-changing Doppler; passes last minutes
Continuous handover between satellites and beams
Coverage needs constellations of hundreds to thousands
Lowest free-space path loss → small user terminals work
Examples: Starlink, OneWeb, Kuiper, Iridium
MEO
2,000–35,786 km (GPS: 20,200 km)
Round-trip latency ~130–250 ms
Moderate Doppler; passes last hours
Global coverage with dozens of satellites
Home of GNSS: GPS, Galileo, GLONASS, BeiDou
O3b/mPOWER (≈8,000 km) for broadband trunking
Middle ground: fewer sats than LEO, less delay than GEO
GEO
35,786 km, equatorial
Appears fixed in the sky → no tracking, cheap fixed dishes
Round-trip latency ~500–600 ms — felt in interactive traffic
Three satellites ≈ global coverage (poles excluded)
Highest path loss (~210 dB at Ka-band)
Decades of broadcast, VSAT, and military heritage
One launch, one orbital slot, 15+ year lifetime
THE ORBIT TRADE
Lower orbit buys latency and link budget but costs constellation size, Doppler compensation, and handover complexity — the same coverage-vs-density trade that drives terrestrial cell shrinkage, played out vertically.
Refs: Tedeschi, Sciancalepore & Di Pietro, Computer Networks 216 (2022) · Salim, Moustafa & Reisslein, IEEE Commun. Surveys & Tuts. 27(1) (2025).
Notes: Latency figures are typical end-to-end user values; bent-pipe vs ISL routing changes LEO numbers slightly.

## Slide 9
Satellite Communications II: The Link
A power-limited channel where every dB is negotiated
L / S / C / X / Ku / Ka / Q-V + optical ISL
10M
100M
1G
10G
100G
1T
Hz
FREQUENCY BANDS
L/S (1–4 GHz): mobile SATCOM, GNSS — rain-tolerant
C (4/6) legacy fixed; X (7/8) military
Ku (12/14) VSAT/DTH; Ka (20/30) HTS; Q/V (40/50) feeders
WAVE CHARACTERISTICS
Free-space path loss dominates: ~210 dB, GEO at Ka
Rain fade grows steeply with band (Ka ≫ C)
Scintillation, low-elevation atmospheric effects
MODULATION & ACCESS
DVB-S2X: QPSK → 32APSK with adaptive coding & modulation
APSK favored: nearly constant envelope suits saturated amps
Military: FHSS at EHF for protected SATCOM; DSSS ranging
POWER
TWTA/SSPA run near saturation for efficiency
Link budget in Eb/N0 and G/T, not raw SNR
Solar-power ceiling caps the whole downlink budget
NOISE & INTERFERENCE
Thermal-noise-limited; antenna temperature matters
Adjacent-satellite interference → coordination regimes (ITU)
Uplink jamming is the classic military threat model
ANTENNA PROPERTIES
High-gain parabolics for fixed GEO
Electronically steered phased arrays track LEO (Starlink terminal)
Multibeam spot arrays on the spacecraft reuse spectrum
APPLICATIONS
Broadband (HTS, LEO megaconstellations), broadcast
GNSS, backhaul, maritime/aero, IoT
Military and government protected comms
BENEFITS & LIMITATIONS
+ Coverage where nothing else reaches
− GEO delay; LEO Doppler + handover; spectrum coordination; cost
→ Converging with terrestrial: 5G NTN puts handsets on satellites
Refs: ETSI EN 302 307-2 V1.3.1, DVB-S2X (2021) · ITU-R Rec. P.676-12 (2019) · Tedeschi et al., Computer Networks 216 (2022).
Notes: SATCOM is the band family where TRANSEC vocabulary (protected SATCOM, EHF hopping) survives in current operational use — bridge to the taxonomy.

## Slide 10
Why the Spectrum March Keeps Going Up
Every band in this deck exists because the one below it ran out of something
WHAT YOU GAIN
Bandwidth: C = B log₂(1+SNR) — capacity scales with B, and contiguous B only exists up-spectrum
Aperture: shorter λ packs more antenna elements into the same area → beamforming gain
Reuse: pencil beams and short range mean the same Hz serves many users
WHAT YOU PAY
Path loss between isotropic antennas grows ~f²; blockage and absorption stack on top
Hardware: PA efficiency, phase noise, and ADC cost all worsen with frequency
Coverage: shorter range forces densification — capex replaces physics
WHAT IT MEANS FOR TRANSEC
Detectability, jamming geometry, and intercept range all change per band
THz absorption and mmWave beams confine energy — covertness by propagation
A physical-layer taxonomy must treat band as a first-class axis, not a footnote
Next: mapping TRANSEC objectives (LPD · LPI · LPE · AJ · TFS) onto each of these bands
Refs: Shannon, Bell Syst. Tech. J. 27 (1948) · CNSSI No. 4009 (2022) · Bash, Goeckel & Towsley, IEEE JSAC 31(9) (2013).
Notes: Closing ties the survey back to the taxonomy: the band attributes on the previous slides become the columns; TRANSEC objectives become the rows.

## Slide 11
References
STANDARDS & SPECIFICATIONS
ISO/IEC 18092:2013 / ECMA-340 — Information technology — Near Field Communication Interface and Protocol (NFCIP-1). ISO/IEC JTC 1/SC 6.
Bluetooth SIG — Bluetooth Core Specification, Version 6.1, May 2025.
IEEE Std 802.11be-2024 — Amendment 2: Enhancements for Extremely High Throughput (EHT) (Wi-Fi 7). IEEE, published July 2025.
3GPP TS 25.211 — UTRA (FDD): Physical channels and mapping of transport channels onto physical channels.
3GPP TS 36.211 — E-UTRA: Physical channels and modulation.
3GPP TS 38.211 — NR: Physical channels and modulation.
ETSI EN 302 307-2 V1.3.1 (2021) — DVB-S2 Extensions (DVB-S2X): framing structure, channel coding and modulation for broadband satellite applications.
ITU-R RECOMMENDATIONS & REPORTS
Rec. ITU-R M.2160-0 (11/2023) — Framework and overall objectives of the future development of IMT for 2030 and beyond (IMT-2030).
Rep. ITU-R M.2541 (2024) — Technical feasibility of IMT in bands above 100 GHz.
Rec. ITU-R P.676-12 (2019) — Attenuation by atmospheric gases and related effects.
PAPERS & GOVERNMENT REFERENCES
C. E. Shannon — “A Mathematical Theory of Communication,” Bell System Technical Journal, vol. 27, 1948.
B. A. Bash, D. Goeckel, D. Towsley — “Limits of Reliable Communication with Low Probability of Detection on AWGN Channels,” IEEE JSAC, vol. 31, no. 9, 2013.
T. S. Rappaport et al. — “Wireless Communications and Applications Above 100 GHz: Opportunities and Challenges for 6G and Beyond,” IEEE Access, vol. 7, 2019.
J. Ma et al. — “Security and eavesdropping in terahertz wireless links,” Nature, vol. 563, pp. 89–93, 2018.
P. Tedeschi, S. Sciancalepore, R. Di Pietro — “Satellite-based communications security: A survey of threats, solutions, and research challenges,” Computer Networks, vol. 216, 2022.
S. Salim, N. Moustafa, M. Reisslein — “Cybersecurity of Satellite Communications Systems: A Comprehensive Survey,” IEEE Communications Surveys & Tutorials, vol. 27, no. 1, 2025.
CNSS — CNSSI No. 4009, Committee on National Security Systems Glossary (TRANSEC definition), 2022.
Notes: All entries verified to exist as of July 2026. Standards cited without a year (3GPP TS series) are living documents — cite the release/version you actually consult in the written taxonomy.